## Slide 1
CAPT Mark Oesterreich, USN
Commanding Officer
NSWC Crane
Dr. Brett Seidle, SES
Technical Director
NSWC Crane
Electronic Parts for Strategic
Systems: Past, Present and Future
David Emily
703-966-5483
davidemily@bluemarble.net

## Slide 2: Requirements
Strategic Weapon Systems electronic parts must meet the most stringent requirements
  Strategic Radiation Hardness
    Prompt Dose Rate upset, recovery and survivability
    Total Ionizing Dose
    Neutron Displacement Damage
    Natural Space Heavy-ion and proton single-event effects
  30+ year typical system life
    Submarine, Silo, Bomber, Bunker environments
  Reliability
    High availability, short-notice operation
  Missile launch
    Shock, vibration, acceleration, pressure, vacuum
  Trust
    Counterfeit to sophisticated tampering
While maintaining affordability, availability and performance

## Slide 3: Declining Rad-Hard Industrial Base
Foreign acquisitions and business changes continue to impact the radiation-hardened electronics industrial base - a long-term trend
  Many rad-hard part manufacturers have exited market
  Low volumes do not attract additional vendors
  Natural-space parts do not satisfy Strategic Rad-Hard Requirements
Strategic Parts Vendors
Year 85 90 10 17 25
Digital 9* 4 2 1 ?
Analog 7* 3 1 0** ?
* From April 2011 presentation by SP23 to OPNAV N87
** High Voltage Analog
Notes: 4
Honeywell , BAE – Digital
Intersil – Analog

## Slide 4: Evolution of Strategic Electronics
Strategic electronics have evolved with industrial base
  Do not typically push leading edge technology
Previous Generation
  1980s Electronics Technology
    Predominately Bipolar Technology (I²L, ISL, TTL)
    10 MHz 16-bit Processor; 16K Static Random Access Memory
    Fusible Link program memory; Plated-wire non-volatile memory
  Captive Line Semiconductors
    Controlled almost everything
    Program unique custom requirements
Current Generation
  2010s Electronics Technology
    Predominately CMOS; Bipolar for High-voltage analog
    100 MHz 32-bit processor; 4M SRAM; 1M Magnetic non-volatile memory
  Procured to Mil-standards
    Qualified Manufacturers List (QML) & Qualified Parts List (QPL)
    Supplemented with program unique requirements testing

## Slide 5: Future Strategic Electronics
What if we totally lose our traditional (Rad-Hard by Process and Design) strategic rad-hard industrial base ?
Alternatives – With increasing risk
  Strategic Radiation-Hardened By Design (S-RHBD)
    Trusted commercial fabrication lines with no process modification
    Design and layout rules added to conventional RHBD to address strategic prompt dose-rate radiation upset, recovery and survivability
  Radiation-Hardened by Design (RHBD) with up-screen
    Trusted commercial fabrication lines with no process modification
    Design and layout rules for space level total dose and single-event effects mitigation
    Intrinsic with up-screen for strategic prompt dose rate effects
  Commercial off-the-shelf (COTS)
    Commercial fabrication line/parts with no modification
    Up-screen for all radiation environments

## Slide 6: Challenges
Strategic and conventional RHBD have challenges
  Fabrication process stability
    Difficult to reduce strategic system 5 to 10 year cycle to model, design, fabricate, qualify, flight qualify and procure entire production quantity
    Commercial fabrication processes undergo “continuous process improvement” for yield, performance and cost with minimal to no consideration for radiation hardness impact
    Possible notification but no influence (except life-of-type-buy)
  Coordination/interface (store-front)
    Multiple parties involved in modeling, design, fabrication, packaging, electrical and radiation testing, qualification of finished product
    No single party accepts responsibility for final product
    Liability, schedule and cost risk fall back on program/prime
  Reliability models do not support 30+ year product life
    Basic reliability models, design and layout rules require modification
  Conventional RHBD does not design for strategic prompt dose rate
    Limited dose rate testing fault coverage may not identify “weak-links”

## Slide 7: Challenges (2)
Commercial Off-the-Shelf has significant challenges
  Fabrication process and design stability
    Difficult to reduce strategic system 5 to 10 year cycle to qualify, flight qualify and procure entire production quantity
    No notification of process or design change
    Parts may be from multiple fabrication lots, further complicating radiation hardness assurance
  Testability and fault coverage
    Unlikely to have access to circuit design details or test vectors to develop adequate fault coverage
    With no design or layout radiation hardening rules for any radiation environments there are likely to be weak radiation hardness areas
    Limited radiation tests and bias conditions give high opportunity for test escapes
  Unlikely to have been designed for 30+ year life
    Reliability testing impacted by same testability and fault coverage issues as radiation testing
    Packaging is likely non-hermetic and also does not support 30+ years

## Slide 8: Challenges (3)
Commercial Off-the-Shelf challenges - continued
  Additional packaging concerns
    Lead-free
    Copper bond wires
    Plastic compounds stability, chemical reactions, outgassing, …
    Flip-chip warm x-ray thermo-mechanical issues

## Slide 9: Summary
Strategic Radiation-Hardened by Design is lowest risk alternative to traditional strategic rad-hard
  Addition of design and layout rules for prompt dose rate survivability, upset and recovery
  Establishment of storefront business model willing to take full responsibility for final product
  Extend reliability models to support 30+ year life
  Long-term availability and stability of fabrication process is remaining challenge
97% of typical strategic system part count are already non-developmental off-the-shelf parts
  13% active discrete transistors and diodes
  84% passive discrete capacitors, resistors, magnetics

## Slide 10: Audience Participation
Are there other Alternatives ?
Are there other Challenges ?
Are some Challenges non-issues ?
What are potential solutions to challenges ?