## Slide 1
NSWC Crane Printed Electronics
Presented by: Steve Vetter
CAPT Mark Oesterreich, USN
Commanding Officer
Dr. Brett Seidle, SES
Technical Director
Statement A: Approved for Public Release; Distribution is unlimited.
Distribution Statement D: Distribution authorized to the Department of Defense and U.S. DoD contractors only.

## Slide 2: Agenda
PCB Manufacturing
Printed Electronics
Activities and Projects
Distribution Statement D: Distribution authorized to the Department of Defense and U.S. DoD contractors only.

## Slide 3: Agenda
PCB Manufacturing
Printed Electronics
Activities and Projects
Distribution Statement D: Distribution authorized to the Department of Defense and U.S. DoD contractors only.

## Slide 4: PCB Manufacturing - Facility
Facility:
Fully government owned and operated
Secure
  Entire fabrication facility is a restricted access area
  Cleared to Secret
16000+ square feet
Class 10K controlled environment cleanrooms
Zero discharge waste treatment system
Distribution Statement D: Distribution authorized to the Department of Defense and U.S. DoD contractors only.

## Slide 5: PCB Manufacturing - Design
CAE Tools:
Ansys SiWave
Ansys IcePak
Polar Speedstack
Admunson Arkeo Stack
CAD Tools:
  PCB Layout:
  Altium
  Mechanical:
  AutoCAD
  FeatureCAM
  MasterCAM
  Solidworks
CAM Tools:
  PCB Tooling:
  Downstream CAM350
  UCAMCO UCAM
  Reverse Engineering:
  ScanCAD
Distribution Statement D: Distribution authorized to the Department of Defense and U.S. DoD contractors only.

## Slide 6: PCB Manufacturing - Capability
Multilayer:
20 layers + Ridged
Sequential lamination
  Buried and blind vias
  Stacked/staggered microvias
High Tg FR4, Teflon, Polyimide
Embedded passives
Flex / Ridged Flex:
8 layers +
Multiple ridged sections
Pyralux, LCP
High Density Interconnect: (in development)
12.5 micron features
Multilayer / sequential lamination
Embedded active and passive
Substrate / interposer / RDL
Distribution Statement D: Distribution authorized to the Department of Defense and U.S. DoD contractors only.

## Slide 7: PCB Manufacturing - Test
Electrical Test
Microcraft EMMA 6161 flying probe
Polar CITS880s Impedance Tester
Hipot Tester (AC/DC/IR) - Sentry 30 Plus (500V)
Inspection
Orbotech Discovery OLB Automatic Optical Inspection System
Siren Hole Checker drilled hole inspection system
CMI Plating thickness measurement
Olympus and Zeiss Metallurgical Microscopes
Distribution Statement D: Distribution authorized to the Department of Defense and U.S. DoD contractors only.

## Slide 8: PCB Manufacturing – QA and Reliability
Quality Assurance:
Microsection
Visual / mechanical Inspection
  Interconnect Stress Test (IST) - IPC TM650 2.6.26
  Insulation Resistance Testing (SIR)
Environmental
  Temperature / humidity cycling
  Vibration
IPC 600/610 Class 3 Certified
Bowman XRF
Analytical Lab:
Auto - titration
UV VIS
Over 300 process controls
Distribution Statement D: Distribution authorized to the Department of Defense and U.S. DoD contractors only.

## Slide 9: Agenda
PCB Manufacturing
Printed Electronics
Activities and Projects
Distribution Statement D: Distribution authorized to the Department of Defense and U.S. DoD contractors only.

## Slide 10: Printed Electronics
Optomec AJ-5X Aerosol Jet Printer
  Full 5-axis 3D printing of conductive and dielectric inks
  Conformal circuitry
  Fully additive interconnect fabrication
  Embedded active devices
  Printed / conformal antennas and sensors
Distribution Statement D: Distribution authorized to the Department of Defense and U.S. DoD contractors only.

## Slide 11: Printed Electronics
Printed Electronics Lab :
FormLabs Formed2 SLA 3D Printer
Voltera V-One
Botfactory Squint
LPKF U3 Protolaser
Digital 3D Microscope 2000x magnification
Laser 3D Confocal Microscope 5nm resolution
Ink Development
  Planetary Ball Grinder
  Viscometer
  4plc analytical scale
  Potentiostat
  Fume hood
  Spin coater
  Vacuum Oven
  Photonic sinter
  system
Distribution Statement D: Distribution authorized to the Department of Defense and U.S. DoD contractors only.

## Slide 12: Agenda
PCB Manufacturing
Printed Electronics
Activities and Projects
Distribution Statement D: Distribution authorized to the Department of Defense and U.S. DoD contractors only.

## Slide 13: PCB and PE Fusion
Explore potential solutions by combining the best of traditional PCB manufacturing with Additive Printed Electronics
Utilize unique combination of capabilities at Crane
Areas of Investigation:
  Planar embedded die interconnects (Direct Write)
  Localized high density packaging fan out
  Counterfeit Mitigation Technologies
  Tamper Mitigation Technologies
Distribution Statement D: Distribution authorized to the Department of Defense and U.S. DoD contractors only.

## Slide 14: Printed Silver/Zinc batteries
Prototype batteries to test inks
Silver/Zinc batteries
1.6V max charge
1.56V working charge
Good cycling ability
Prototypes can be cycled 20 times before decay of charge
Main issue is electrolyte storage and delivery and separator failure
Linked in series to power 2V LED
Battery Printed via Optomec
High internal impedance
Can be solved with different design
Cycles well but low charge storage
More “fingers” of reduced size will
Result in higher charge
Only possible to print this design
Using the optomec
Distribution Statement D: Distribution authorized to the Department of Defense and U.S. DoD contractors only.

## Slide 15: Printed Sensors
3-D printed flexible sensors for use in detection of environmental changes and agent detection
Sensors are printed using Optomec instrument or using graphite based inks
Polymeric coatings induce a capacitance change when encountering a chemical element
Allows for the fabrication of lightweight, low-power, flexible sensors
Distribution Statement D: Distribution authorized to the Department of Defense and U.S. DoD contractors only.

## Slide 16: Printed Sensors
Gen 1 and Gen 2 thermal sensors
Constructed from printed silver
Resistance based
Can be coated in protective polymer
Highly repeatable readings
Flexible
Sensor Designs
Can be capacitance or resistance based
Top and middle designs are silver printed via Optomec and then coated in a respective polymer
Can suffer from hysteresis depending on polymer
Leads to flexible humidity sensor
Bottom design is a thin polymer film coated in graphite
Good repeatability if hydrophobic polymer is used
Chart: Resistance (Ohms)
| 832 | 839 | 849 | 857 | 867 | 877 | 887 | 896 | 906 | 916 | 926 | 935 | 944
A | 20.7 | 25.4 | 30.5 | 35.6 | 40.3 | 45.2 | 50.4 | 55.3 | 60.3 | 65.5 | 70.1 | 75.2 | 80
B | 20.7 | 25.4 | 30.5 | 35.6 | 40.3 | 45.2 | 50.4 | 55.3 | 60.3 | 65.5 | 70.1 | 75.2 | 80
C | 20.7 | 25.4 | 30.5 | 35.6 | 40.3 | 45.2 | 50.4 | 55.3 | 60.3 | 65.5 | 70.1 | 75.2 | 80
D | 20.7 | 25.4 | 30.5 | 35.6 | 40.3 | 45.2 | 50.4 | 55.3 | 60.3 | 65.5 | 70.1 | 75.2 | 80
Chart: PVA coated Optomec
| 37.5 | 49.4 | 58.2 | 70.5 | 76.599999999999994 | 82.7
 | 9470000 | 9210000 | 320100 | 108800 | 84200 | 45530
Distribution Statement D: Distribution authorized to the Department of Defense and U.S. DoD contractors only.

## Slide 17: Ferrofluid Energy Harvesters
Objective
    Develop flexible/wearable energy harvesters for realizing self-powdered flexible electronics
      Desired characteristics: small, flexible, stretchable
      Use a printed battery /supercapacitor or other energy storage devices to ensure energy harvesting flexibility and power supply stability/reliability
    Current status
    Parameter modeling is performed to optimize the variables (such as wire windings, magnetic positioning, vibration amplitude and frequency, ferrofluid properties) for tuning output voltage of flexible ferrofluid energy harvesters
    Three ferrofluids have been formulated to match with different sizes/shapes of magnets as the magnetic media
    Several energy harvesters have been developed generating output voltages up to 30 volts; have illuminated an array of LED lights; and have powered thermal sensors.
Next step
  Fabricate thin planar flexible ferrofluid energy harvesters suitable for the frequency range from 1 to 60 Hz
  Develop assembly process to integrate the energy harvester to the flexible/wearable electronics
Power a thermal sensor
Illuminate LED
Flexible chamber energy harvester designs
Distribution Statement D: Distribution authorized to the Department of Defense and U.S. DoD contractors only.

## Slide 18: Common FHE Sensor Architecture
ADC
µCtlr
Blue Tooth
Sensor
Element
Stimulus
Wireless Data Link
Thinned active die
Flexible substrate
Printed interconnects and passive components
Common Backend Architecture
Distribution Statement D: Distribution authorized to the Department of Defense and U.S. DoD contractors only.

## Slide 19: Advanced Additive Packaging
Cut-away view of underside of Channel
Cross Section of T/R Module Test Vehicle
Alternative Jet Impingement Cooling
  Liquid Cooling Application
  Enables cooling fluid to be in direct contact with HPA MMIC
  May enable more efficient RF Interconnect
  Jet Impingement Cooling may provide up to 57%1 higher heat transfer between cooling fluid and MMIC
  Transitioned to Agency Directed NextFlex Project
1. M. Shaw, J. Waldrop, et al, "Enhanced thermal management by direct water spray of high-voltage high power devices …”, Proc. IEEE Inter Soc. Conf. Therm. Phenom, pp. 1007-1014, June 2002.
Distribution Statement D: Distribution authorized to the Department of Defense and U.S. DoD contractors only.

## Slide 20: Additively Manufactured PCB
Floor plan for Crane facility approximately 16,000 ft2
3D Printer
Screen Print
Oven
Planarizer
Drill / Post Process
~250 ft2
Distribution Statement D: Distribution authorized to the Department of Defense and U.S. DoD contractors only.
Notes: PCB’s are the foundation of most electronic systems.
Manufacturing is a complex sequence of photolithographic, chemical and mechanical processes using specialized equipment in a dedicated facility.
Generates waste – long lead times
This investigation explores combining 3D printing with conductive paste to yield:
  Reduction in Process Steps – from >50 to < 10
  Eliminate waste – no water or chemical processes
  Facilitate point of use manufacturing – small foot print
  Multipurpose equipment and materials

## Slide 21: Additively Manufactured PCB
Distribution Statement D: Distribution authorized to the Department of Defense and U.S. DoD contractors only.
Patent No. US 10,070,532 B2
Notes: Final result:
Pads, conductors, through connects
Ready for assembly
Assembled one sample using conductive silver adhesive
ABS like dielectric does not hold up to eutectic solder temperatures

## Slide 22: NextFlex DataCube
  Problem:
  Design cycle for Printed Electronics (PE) needs to evolve into an integrated design workflow
    Processes are not standardized
    Material properties vary with process conditions
  Current design flow requires direct designer knowledge and fabrication process interaction
  Linkage between material, process, and properties has been termed a “datacube”
  NextFlex Manufacturing Innovation Institute has initiated the “DataCube Project” to address the material-process-property data gap through the creation of a database.
Figure 1: NextFlex vision for FHE Full Stack Design Flow
Figure 2: Aerosol Jet Printing
Distribution Statement D: Distribution authorized to the Department of Defense and U.S. DoD contractors only.

## Slide 23: Contact
For questions please contact Steve Vetter
  Office: (812)854-4074
  Mobile: (812)227-9422
  Email: stephen.vetter@navy.mil
Distribution Statement D: Distribution authorized to the Department of Defense and U.S. DoD contractors only.